## Slide 1
From Spectra to Matrix: a practical overview
Silvia Mari
Ospedale San Raffaele
mari.silvia@hsr.it

## Slide 3
Robert A van den Berg et al. BMC Genomics 2006, 7:142
Margriet M.W.B. Hendriks et al. Trends in Analytical Chemistry, Vol. 30, No. 10, 2011
Andrew Craig et al. Anal. Chem. 2006, 78, 2262-2267
PEAK ALIGNMENT
BINNING
DATA PRETREATMENT:
SCALING
CENTERING
TRANSFORMATIONS
Notes: In metabolomics research, there are several steps between
the sampling of the biological condition under study and
the biological interpretation of the results of the data analysis
(Figure 1). First, the biological samples are extracted
and prepared for analysis. Subsequently, different data
preprocessing steps [3,5] are applied in order to generate
'clean' data in the form of normalized peak areas that
reflect the (intracellular) metabolite concentrations.
These clean data can be used as the input for data analysis.
However, it is important to use an appropriate data pretreatment
method before starting data analysis. Data pretreatment
methods convert the clean data to a different
scale (for instance, relative or logarithmic scale). Hereby,
they aim to focus on the relevant (biological) information
and to reduce the influence of disturbing factors such as
measurement noise. Procedures that can be used for data
pretreatment are scaling, centering and transformations.

## Slide 4
Fast Fourier Transform Cross-Correlation Methods
address the variable correspondence problem across large sample cohorts common in metabolomic/metabonomic studies
PEAK ALIGNMENT
BINNING
2005 Application of Fast Fourier Transform Cross-Correlation for the Alignment of Large Chromatographic and Spectral Datasets
Jason W. H. Wong, Caterina Durante, and Hugh M. Cartwright
Anal. Chem., 2005, 77 (17), pp 5655–5661 DOI: 10.1021/ac050619p
2010 icoshift: A versatile tool for the rapid alignment of 1D NMR spectra
Savorani F, Tomasi G, Engelsen SB
Journal of Magnetic Resonance 2010, 202(2):190-202 [PMID: 20004603]
2011 An integrated workflow for robust alignment and simplified quantitative analysis of NMR spectrometry data
Trung N Vu et al.
BMC Bioinformatics 2011, 12:405 http://www.biomedcentral.com/1471-2105/12/405
2012 Variable Reference Alignment: An Improved Peak Alignment Protocol for NMR Spectral Data with Large Intersample Variation
Neil MacKinnon et al.
Analytical Chemistry ahead of print. dx.doi.org/10.1021/ac301327k

## Slide 5
Brain extracts
Conditioned cell media
PEAK ALIGNMENT
BINNING

## Slide 6
PEAK ALIGNMENT
BINNING
Binning is a strategy for data reduction
but…
Spectral binning
Rudd, TR et al. Analyst, 2011, 136, 1380
PCA was performed on a wide spectral region, 6.00–1.95 ppm (with regions 4.912–4.730, 3.881–
3.868, 3.680–3.633, 3.363–3.355 and 3.010–2.220 ppm were excluded)
[CPU demanding]
Notes: Historically, pattern recognition of NMR-based
metabolite data was performed using either quantitative or scored
integrals of specific spectral peaks.16,17 This approach does not
work well in crowded regions of spectra with substantial peak
overlap and is not easily automated for application to large sample
sets. Calculating the peak areas within specified segments of a
spectrum (binning or bucketing) was introduced originally to allow
comparison of NMR data measured at different magnetic field
strengths by minimizing but not eliminating the effects of secondorder
spectral differences.18 In NMR-based metabonomic studies,
it also reduces the effect of pH-induced changes in chemical shift, A typical bin width of 0.04 ppm is frequently used for 1H NMR
spectra of urine as it is a good compromise between resolution
and the difficulties related to positional variation in the position
of some analyte species NMR peaks, most notably those of citrate,
which are a function of pH and ionic strength of the sample

## Slide 7
Regular binning
Variable size binning
GSD peak binning
Complex Mixture of properly aligned spectra;
Suitable to be implemented in automatic statistical analysis (no prior information of peak positions) and for model construction and use
Complex Mixture (typically more than 50 components);
Suitable when dealing with similar spectra and small variation have to be detected (prior information of peak positions is an advantage).
Suitable as regular binning when dealing with complex mixtures;
Particular useful when dealing with peak shifts difficult to be aligned with standard tools.
PEAK ALIGNMENT
BINNING
Binning is a strategy for data reduction
[and removal of unwanted spectral regions]

## Slide 8
REGULAR
VARIABLE
GSD
it is the most common strategy used (both NMR software and math/stat software)
normally it is well implemented and gives data matrix straightforwardly

## Slide 9
REGULAR
VARIABLE
GSD
difficult to automatize, normally binning regions have to be defined (graphically) by the user.
normally it is implemented as standard integration tool, where integral regions are applied toa serie of spectra
lots of effort devoted to the automatic regions detection

## Slide 10
REGULAR
VARIABLE
GSD
Spectral binning VS Peak list binning
it bases on deconvoluted peaks obtained by GSD algorithm developed by Stan Sykora
[REF. S.Sykora, C.Cobas, Peak Shapes in NMR Spectroscopy, www.ebyte.it/stan/Talk_MMCE_2009.html; C.Cobas, S.Sykora, The Bumpy Road Towards Automatic GSD, Poster at 50th ENC, DOI 10.3247/sl3nmr09.003]

## Slide 11
ppm Intensity Width Area
1 1.642 130.7 4.46 4163.16
2 1.646 49.9 2.67 949.46
3 1.653 218.0 5.39 8390.45
4 1.664 83.3 2.86 1701.71
5 1.675 50.2 1.95 699.60
6 1.689 252.4 4.86 8763.26
7 1.703 547.9 8.18 31999.22
8 1.716 716.4 5.67 28970.94
9 1.727 312.5 4.99 11120.21
10 1.740 313.1 5.15 11509.43
11 1.750 107.1 7.25 5544.77
REGULAR
VARIABLE
GSD
Spectral binning VS Peak list binning

## Slide 12
1.3 726.099 652.391 741.904 897.865 541.909
1.35 2518.3 2724.25 2767.09 3179.39 8757.55
1.4 643.564 622.997 605.02 785.784 713.88
1.45 698.496 693.145 717.695 896.104 725.432
1.5 995.557 1035.99 1061.42 1283.57 1206.83
1.55 523.029 497.019 513.755 683.519 515.426
1.6 624.478 608.938 659.421 816.91 640.05
1.65 768.886 759.836 834.469 1002.1 767.783
Spectral binning
(regular bucketing)
Generation of the matrix BxS
(B are the number of bins and S are the number of spectra)
8.85 8.8 8.75 8.7 8.65 8.6 8.55 8.5 8.45 8.4
0 0 0787.135 0 0 0 8217.11 715.193 0 0 0 0
0 0 1034.65 0 0 0 0 1277.02 0 0 0 0
0 0 969.88 0 0 0 0 1594.96 0 0 0 0
0 0 1092.48 0 0 0 5637.08 1052.6 0 0 0 0
0 0 3080.26 0 0 7410.8 0 0 0 0 0 0
0 0 5833.42 0 0 0 7761.06 0 0 3817.87 0 0
0 0 3562.26 0 0 3378.11 0 0 0 0 0 0
0 0 3698.77 0 0 0 5993.16 0 0 0 0 0
0 0 5192.41 368.962 0 1649.74 0 0 0 0 2898.13 0
Generation of the matrix PBxS
(PB are the number of bins and S are the number of spectra)
ppm Intensity Width Area
1 1.642 130.7 4.46 4163.16
2 1.646 49.9 2.67 949.46
3 1.653 218.0 5.39 8390.45
4 1.664 83.3 2.86 1701.71
5 1.675 50.2 1.95 699.60
6 1.689 252.4 4.86 8763.26
7 1.703 547.9 8.18 31999.22
8 1.716 716.4 5.67 28970.94
9 1.727 312.5 4.99 11120.21
10 1.740 313.1 5.15 11509.43
11 1.750 107.1 7.25 5544.77
Peak table binning
REGULAR
VARIABLE
GSD
Spectral binning VS Peak list binning

## Slide 13
PCA
1, 2 and 3 are the three classes used . They correspond to the spectra of stem cells’ culture media, respectively at three different seeding conditions (2 double of 1 and 3 triple of 1). Binning width was 0.05ppm. All spectra were normalized for the total intensity and pareto scaled prior to multivariat statistical analysis.
PLS-DA
OPLS-DA

## Slide 14
DATA PRETREATMENT:
(NORMALIZATION)
CENTERING
SCALING
TRANSFORMATIONS
“The variation in the data resulting from a metabolomics experiment is the sum of the induced variation and the total uninduced variation. The total uninduced variation is all the variation originating from uninduced biological variation, sampling, sample work-up, and analytical variation.” [Robert A van den Berg et al. BMC Genomics 2006, 7:142]

## Slide 15
DATA PRETREATMENT:
(NORMALIZATION)
CENTERING
SCALING
TRANSFORMATIONS
Normalization. This is a row operation that is applied to the data from each sample and comprises methods to make the data from all samples directly comparable with each other. A common use is to remove or minimize the effects of variable dilution of the samples.
[Andrew Craig et al. Anal. Chem. 2006, 78, 2262-2267]
Normalization by sum
Normalization by median
Normalization by a reference sample
Normalization by a reference feature
Sample specific normalization (i.e. dry weight, volume)

## Slide 16
DATA PRETREATMENT:
(NORMALIZATION)
CENTERING
SCALING
TRANSFORMATIONS
Centering. Centering converts all the concentrations to fluctuations around zero instead of around the mean of the metabolite concentrations. Hereby, it adjusts for differences in the
offset between high and low abundant metabolites.
[Robert A van den Berg et al. BMC Genomics 2006, 7:142]
RAW-WISE METHODs

## Slide 17
DATA PRETREATMENT:
(NORMALIZATION)
CENTERING
SCALING
TRANSFORMATIONS
Scaling. Scaling methods are data pretreatment approaches that divide each variable by a factor, the scaling factor, which is different for each variable
[Andrew Craig et al. Anal. Chem. 2006, 78, 2262-2267]
Two scaling subclasses:
data dispersion as a scaling factor (such as, the standard deviation)
size measure as a scaling factor (for instance, the mean)
COLUMN-WISE METHODs

## Slide 18
DATA PRETREATMENT:
(NORMALIZATION)
CENTERING
SCALING
TRANSFORMATIONS
Two scaling subclasses:
data dispersion as a scaling factor (such as, the standard deviation)
size measure as a scaling factor (for instance, the mean)

## Slide 19
DATA PRETREATMENT:
(NORMALIZATION)
CENTERING
SCALING
TRANSFORMATIONS
Heteroscedasticity. In data analysis it is often assumed that the total uninduced variation resulting from biology, sampling, and analytical measurements is symmetric around zero with equal standard deviations. However, this assumption is generally not true. For instance, the standard deviation due to uninduced biological variation depends on the average value of the measurement. This is called heteroscedasticity
[Andrew Craig et al. Anal. Chem. 2006, 78, 2262-2267]
Application. Samples that typically show high variability in concentration, and the derived metabolic profiles have a heteroscedastic noise structure characterized by increasing variance as a function of increased signal intensity. (test to verify heteroscedastic’s hypothesis should be performed, see Goldfeld-Quandt test)

## Slide 20
Data after CENTERING
AUTO SCALING
ORIGINAL DATA
PARETO SCALING
RANGE SCALING
VAST SCALING
LEVEL SCALING
LOG TRANSFORMATION
POWER TRANSFORMATION

## Slide 21
PEAK ALIGNMENT
BINNING
DATA PRETREATMENT:
(NORMALIZATION)
CENTERING
SCALING
TRANSFORMATIONS

## Slide 22
ACKNOWLEDGMENTS
Alessandra Boletta
Roberto Sitia
Simone Cenci
Francesco Camnasio
Gianvito Martino
Jose Garcia Manteiga
Francesca Fontana
Giovanna Musco
Andrea Spitaleri
Michela Ghitti
Dimitrios Spiliotopoulos
Edoardo Gaude
Valeria Mannella
Mestrelab Team
Stanislav Sykora
$